## Slide 1
Week 9–10 Report
SoC Bring-Up
Progress
March 18–21, 2026 · bringup_v1
RISC-V CNN Accelerator · Hummingbird E203 · NICE Interface

## Slide 2
OVERVIEW
What We Cover
Bring-up timeline: Mar 18–21
Key breakthrough: NICE encoding fix
Phase closure status (3 / 4 / 5)
Validation results
Current blockers & next steps

## Slide 3
PROGRESS
Day 1 — Mar 18
✓
Clone main repo & SoC repo (e203_hbirdv2 fork)
✓
Configure GitHub SSH for private repos
✓
Create & switch to branch bringup_v1
✓
Install simulation tools: iverilog, gtkwave, verilator
✓
Verify ./Project_Manager.sh gen_model runs
✓
Verify ./Project_Manager.sh run_hw runs

## Slide 4
PROGRESS
Day 2 — Mar 19
✓
Python reference model gen_model verified ✓
✓
RTL simulation run_hw verified ✓
✓
Fix cnn_nice_core.v: add busy signal & result_valid flag
✓
Fix cnn_nice_core.v: add load masks for WLOAD/DLOAD
✓
Fix cnn_nice_core.v: gate COMP / RSTAT with load-complete state
✓
Extend tb_cpu_mock.v: illegal index, boundary, partial-load safety cases

## Slide 5
KEY BREAKTHROUGH
Day 3 — Mar 20
✓
Freeze E203 source baseline to official riscv-mcu/e203_hbirdv2
✓
Root-cause analysis: funct3 was wrong selector — NICE uses bits[14:12] for xd/xs1/xs2
✓
Move selector to funct7 per official E203 NICE spec
✓
Install Nuclei GNU toolchain 2024.06
✓
Compile first ELF with CNN NICE instructions — success ✓
✓
Phase 2 (Safety Validation) CLOSED → Version V1.6

## Slide 6
PROGRESS
Day 4 — Mar 21
✓
Phase 3 (Software Path) CLOSED — RSTAT=320 confirmed in full SoC sim ✓
✓
Phase 4 (SDK Portability) CLOSED — nuclei-sdk patch exported ✓
✓
Phase 5 (Board Prep) baseline established ✓
✓
Target locked: SOC=evalsoc, CORE=n300, BOARD=nuclei_fpga_eval, DOWNLOAD=ilm
✓
OpenOCD confirmed at /usr/bin/openocd
✓
Complete VIVADO_FPGA_HANDOFF.md & WORK_DELIVERY_SUMMARY.md → Version V1.8

## Slide 7
KEY BREAKTHROUGH
NICE Encoding Fix
BEFORE (Wrong)
funct3 used as instruction selector
E203 NICE does NOT use funct3 for this.
opcode
funct7
rs2
rs1
funct3
rd
opcode
[ WRONG SELECTOR ]
AFTER (Correct)
Selector moved to funct7[6:5]
xspec (bit25) flags extended opcode.
opcode
funct7
rs2
rs1
funct3
rd
opcode
[ CORRECT SELECTOR ]
→ Full SoC RSTAT=320 confirmed — software stack validated

## Slide 8
STATUS
All Pre-Board Phases Closed
Phase 2
Safety Validation
Mock TB + official lightweight NICE TB, 8 safety cases, V1.6
Closed ✓
Phase 3
Software Path
Nuclei SDK + toolchain 2024.06, full SoC RSTAT=320 confirmed
Closed ✓
Phase 4
Portability & Regression
SDK patch exported, one-command regression validated
Closed ✓
Phase 5
Board Bring-Up Baseline
Target: evalsoc + n300 + ilm, openocd installed
Baseline ✓

## Slide 9
VALIDATION
All Pre-Board Tests Pass
✓
Normal operation path
✓
Negative & boundary values
✓
Invalid load index rejection
✓
Partial load before COMP blocked
✓
Illegal funct3 / opcode → nice_rsp_err=1
✓
Reset clears all state
✓
Full SoC RSTAT=320 confirmed in official E203 RTL
All 7 tests green — ready for first hardware session

## Slide 10
CURRENT BLOCKERS
What Stands Between
Us & Board
JTAG / FTDI Hardware
lsusb does not show device 0403:6010 yet — hardware not connected or driver missing
UART Path
SERIAL_DEV not yet locked — need to confirm /dev/ttyUSB* path
FPGA Board Target
mcu200t vs ddr200t not yet decided — need to choose board shell
All pre-board simulation gates are passing ✓

## Slide 11
ROADMAP
Next Steps
Connect JTAG/FTDI hardware — confirm lsusb shows 0403:6010
Lock UART path — identify /dev/ttyUSB* for serial console
Decide FPGA board target: mcu200t or ddr200t
Run pre-board verification sweep before first hardware session

## Slide 12
Software Stack
Validated.
Hardware bring-up is next.
Version V1.8 · Branch bringup_v1 · Week 9–10