## Slide 1
SoC Bring-Up Report
RISC-V CNN
Accelerator
Hummingbird E203 · NICE Interface · 4×4 INT8 PE Array
March 2026 · bringup_v1

## Slide 2
OVERVIEW
What We Cover
Project overview & system architecture
System block diagram & 4×4 PE array detail
NICE protocol handshake & instruction encoding
Bring-up timeline: Mar 18–21
Phase 3 / 4 / 5 closure
Current blockers & next steps

## Slide 3
ARCHITECTURE
System Block Diagram
RISC-V CORE
Hummingbird E203
RV32IMAC · Nuclei
32-bit · 2-stage pipeline
ITCM + DTCM
CLINT · ECLIC · PWM
→
NICE
req/rsp
xspec/funct7
INTERFACE
NICE
Valid / Ready
Handshake
→
NICE
req/rsp
ACCELERATOR
4×4 PE Array
INT8 · Output Stationary
PE[00]
PE[01]
PE[02]
PE[03]
PE[10]
PE[11]
PE[12]
PE[13]
PE[20]
PE[21]
PE[22]
PE[23]
PE[30]
PE[31]
PE[32]
PE[33]
×4 cols each
EXTERNAL MEMORY (ITCM / DTCM)
CLEAR WLOAD DLOAD COMP RSTAT

## Slide 4
ARCHITECTURE
4×4 PE Array — Dataflow
Processing Element
A_in
INT8 act
W_in
INT8 wt
MAC
INT8×INT8 → INT32
ACC
INT32
partial sum
Each PE: INT8×INT8 → INT32 accumulator
4×4 Array Layout
OUTPUT STATIONARY · ROW×COL BROADCAST
PE[00]
W[0]·A[0]
PE[01]
W[1]·A[0]
PE[02]
W[2]·A[0]
PE[03]
W[3]·A[0]
PE[10]
W[0]·A[1]
PE[11]
W[1]·A[1]
PE[12]
W[2]·A[1]
PE[13]
W[3]·A[1]
PE[20]
W[0]·A[2]
PE[21]
W[1]·A[2]
PE[22]
W[2]·A[2]
PE[23]
W[3]·A[2]
PE[30]
W[0]·A[3]
PE[31]
W[1]·A[3]
PE[32]
W[2]·A[3]
PE[33]
W[3]·A[3]
• Weight: broadcast per column — 4 PE share same W
• Activation: broadcast per row — 4 PE share same A
• Output: accumulated per PE → partial sum
• Throughput: 16 MAC/cycle

## Slide 5
INTERFACE
NICE Protocol — Signals & Encoding
Signal
Dir
Description
nice_req_valid
CPU→Acc
Request valid, payload ready
nice_req_ready
Acc→CPU
Accelerator ready to accept
nice_req_bits
CPU→Acc
opcode / rs1 / rs2 / rd
nice_rsp_valid
Acc→CPU
Response valid
nice_rsp_ready
CPU→Acc
CPU ready to accept response
nice_rsp_bits
Acc→CPU
Result / status / err
Instruction Encoding (RISC-V R-type)
31:25
24:20
19:15
14:12
11:8
7
6:0
opcode'
rs2
rs1
xd/xs1/xs2
funct3
rd
opcode
• xspec (bit 25): extended opcode flag
• funct7[6:5]: selects CLEAR / WLOAD / DLOAD / COMP
• RSTAT=320 confirms full SoC path validated

## Slide 6
PROGRESS
Bring-Up Timeline
MAR 18
Repo cloned · SSH configured · Branch bringup_v1 created · Simulation tools installed
MAR 19
Python model & RTL sim verified · cnn_nice_core.v fixed (busy, result_valid, load masks)
MAR 20
NICE encoding fixed (funct3 → funct7) · Nuclei toolchain 2024.06 · Phase 2 closed → V1.6
MAR 21
Phase 3/4/5 closed · SDK regression ready · FPGA handoff doc · V1.8

## Slide 7
KEY BREAKTHROUGH
NICE Encoding Fix
THE PROBLEM
funct3 was used as the instruction selector
ROOT CAUSE
E203 NICE uses bits [14:12] for xd / xs1 / xs2, not funct3. Selector must live in funct7.
THE FIX
Selector moved to funct7 · Confirmed RSTAT = 320
→ Full SoC simulation now reproduces expected behavior

## Slide 8
PHASE STATUS
All Pre-Board Phases Closed
Phase 3
Software Path
Closed ✓
Phase 4
Portability & Regression
Closed ✓
Phase 5
Board Bring-Up Baseline
Baseline ✓
Target: evalsoc + n300 + ilm · openocd installed

## Slide 9
VALIDATION
All Tests Pass
✓
Normal operation path
✓
Negative & boundary values
✓
Invalid load index rejection
✓
Partial load before COMP blocked
✓
Illegal funct3 / opcode → nice_rsp_err=1
✓
Reset clears all state
✓
Full SoC RSTAT=320 confirmed

## Slide 10
CURRENT BLOCKERS
What Stands Between
Us & Board
JTAG / FTDI Hardware
lsusb does not show device 0403:6010 yet
UART Path
SERIAL_DEV not yet locked
FPGA Board Target
mcu200t vs ddr200t not yet decided
All pre-board simulation gates are passing

## Slide 11
ROADMAP
Next Steps
Connect / pass-through JTAG hardware, confirm lsusb visibility
Lock SERIAL_DEV UART path
Finalize FPGA board target (mcu200t / ddr200t)
Run pre-board verification sweep before first hardware session

## Slide 12
Software Stack
Validated.
Hardware bring-up is next.
RISC-V E203 · NICE · 4×4 INT8 PE Array
Version V1.8 · Branch bringup_v1